| TOOL AND MACHINERY GUIDE 402-253-2772 WEBSITE: WCWRAIL.COM |
| --- |
| Title: Air Brake Hose Storage Racks | Prepared By: Wulf's Custom Welding |
| Document No: 0385 & 0385-1 | Date: April 1, 2014 |

### SUBJECT: AIR BRAKE HOSE STORAGE RACKS

### Capacity: These storage racks have a rated capacity of 500 Lbs.

### FIGURE 1 – 0385- STANDARD VERSION

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: Trainline Hose Only – 0385 (Figure 1)

Trainline & Locomotive Auxiliary Hoses – 0385-1                (Figure 2)

Storage Rack Weight:  290 Pounds

Base Construction Material: Steel

### DESCRIPTION:

### The standard (0385) two-tier rack is designed to store up to sixty each Trainline Air Brake Hoses. The upper tier of the standard rack may be used to store longer intermediate type hoses. The locomotive version (0385-1) is designed to hold 30 Trainline Air Brake Hoses, and 33 Locomotive Auxiliary Hoses. They are both equipped with four each anchor plates to secure the racks to the ground.

INSTRUCTIONS FOR USE:

- Inspect the rack periodically. Make sure all of the assembly bolts are tight and there are no broken welds. If the rack is anchored to the ground, check the securing bolts to make sure they are tight.

- Place air hoses in the rack with the 1-1/4" male pipe fitting facing upward. Make sure the protective shipping cap is in place on the fitting and the glad hand. Depending on the brand of hose, the hose may be stored using the crimps in the ferrule, or by placing the bottom of the ferrule on top of the storage bar.

- Remove the air hoses from the rack for use as necessary. Use caution not to inadvertently knock hoses off the bottom tier if you are removing them from the top tier.

FIGURE 2 – 0385-1 – LOCOMOTIVE VERSION

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with all current Safety rules and requirement.

- WARNING: Keep your feet out from under the rack when placing or removing hoses in the rack.

- WARNING: Do not store longer hoses on the lower rack tier.