| TOOL AND MACHINERY GUIDE 402-253-2772 WEBSITE: WCWRAIL.COM |
| --- |
| Title: EMD And GE Locomotive Car Body Door Retainers | Prepared By: Wulf's Custom Welding |
| Document No. 0207 | Date: June 21, 2010 |

SUBJECT:  EMD AND GE LOCOMOTIVE CAR BODY DOOR RETAINERS

Capacity: Use to hold EMD and GE Locomotive car body doors in the open position to prevent inadvertent closure on employees while performing repairs.

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: EMD Right Hand – 0207

EMD Left Hand – 0208

GE Universal – 0209

Fixture Weight: Less Than 1 Pound Each

Construction Material: Steel

### DESCRIPTION:

### These retainers are designed to fit over the hinges of all styles and models of EMD or GE locomotive car body doors. They prevent car body doors from inadvertently being pushed or blown into employees while performing work on locomotives. They have no other intended uses.

INSTRUCTIONS FOR USE:

EMD AND GE LOCOMOTIVE CAR BODY DOOR RETAINERS:

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repairs on locomotives.

- Inspect the retainer fixtures for defects prior to use. Make sure the cross bar is securely attached, and the bars are not deformed.

- Take the appropriate EMD of GE retainers with you to the locomotive requiring repair. Place them in your pocket or lay them on the running board and pick them up after you have climbed onto the locomotive. Do not attempt to climb up or down locomotive steps with the retainers in your hand.

- Open the car body door and swing it outward until it is in its fully open position (Figure 1).

- Place one retainer over the top hinge of the open door. The cross bar will always face outward toward the handrails (Figure 1).

- When retaining EMD doors, you must apply either the right or left hand retainer as required. The GE retainer is universal.

- The second, pivoting door on GE locomotives will strike the handrail before it will be able to contact the operator.

- When repairs are completed, remove the retainers from the door hinge and place them back into your pocket or lay them on the running board and climb down the locomotive steps.

- Remove all blue flag protection, chocks, and release the hand brake if the freight car is ready to return to service.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with current Safety and General Conduct Rules.

- WARNING: Follow all prescribed safety rules when climbing into or off of locomotives. Always maintain a three-point contact.  Never attempt to climb up or down locomotive steps with the retainers in your hand.

- CAUTION: Never use the retainers for any application other than holding open locomotive car body doors.