| TOOL AND MACHINERY GUIDE 402-253-2772 WEBSITE: WCWRAIL.COM |
| --- |
| Title: Cart Mounted Hydraulic Coupler Jack | Prepared By: Wulf's Custom Welding |
| Document No. 0309 | Date: May 7, 2010 |

### SUBJECT:  CART MOUNTED HYDRAULIC COUPLER JACK

### Capacity: This cart is used to jack couplers for the application of shims. It has no other intended uses. The rated capacity is 3,000 Lbs.

| FIGURE 1 FIGURE 2 |  |
| --- | --- |

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: 0309

Fixture Weight: 76 Pounds

Base Construction Material: Steel Cart With Hydraulic Cylinder

### DESCRIPTION:

### This cart is used to hydraulically lift couplers for shim application. It has no other intended uses.

INSTRUCTIONS FOR USE:

COUPLER JACKING AND SHIM APPLICATION:

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repair work.

WARNING: Ensure car(s) is/are properly secured with hand brakes before attempting to perform coupler removal or installation.

- Inspect the cart and hydraulic jacking system. Repair or replace the jack if it is leaking more than a few drops of hydraulic fluid. Make sure the jack base is securely attached to the cart (Figure 1).

- With the cylinder fully retracted, move the cart under the coupler to be raised. The lifting head of the jack should be placed directly under and in full contact with the knuckle (Figure 3).

- Close the release valve by turning it clockwise, and begin jacking using the foot operated pump pedal. The pedal is equipped with a spring to provide automatic pedal return (Figure 2).

- Continue jacking the coupler until in contacts the draft arm. Stop jacking after contact is made Keep your hands and fingers away from the coupler and draft arm area during extension.

- Apply and affix the necessary shims under the coupler .

- Slowly turn the release valve counter-clockwise to gradually release hydraulic pressure and lower the coupler (Figure 2).  The release valve should only be operated by hand. Keep your hands and fingers away from the coupler and draft arm during retraction.

FIGURE 3

- When the coupler has retracted far enough to contact the shim, open the release valve further to speed up final retraction.

- Inspect the jacking system and place it back into its normal place of storage.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees.

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with all Safety Requirements.

- WARNING: Never place your hands or fingers near the coupler during extension or retraction.

- CAUTION: Never use the Coupler Jacking system for any purpose other than raising and lowering couplers.

- CAUTION: Use your hand to operate the release valve. Using your foot to could cause valve or valve handle damage.