| TOOL AND MACHINERY GUIDE 402-253-2772 WEBSITE: WCWRAIL.COM |
| --- |
| Title: Locomotive Turbocharger Spin Pole | Prepared By: Wulf's Custom Welding |
| Document No. 0302 | Date: May 7, 2010 |

SUBJECT: LOCOMOTIVE TURBOCHARGER SPIN POLE

Capacity: This tool does not require a rated capacity.

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Omaha, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: 0302

Approximate Weight: Less Than 1 Pound

Construction Material: Aluminum Pole With Plastic Contact Rod

### DESCRIPTION:

### This pole is used to spin Locomotive Turbochargers for inspection. It may be used with either EMD or G.E. locomotives. It has no other intended uses.

INSTRUCTIONS FOR USE:

LOCOMOTIVE TURBOCHARGER SPIN POLE:

WARNING: Ensure locomotive(s) is/are properly secured with hand brakes and/or chocks before attempting to perform Locomotive Turbocharger Inspection.

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repairs.

- Inspect the pole for defects. The telescoping handle must move freely. The Retention Screw and Detent Pin must be in place (Figure 1).

- With the pole retracted, place it into the Locomotive Bag Filter Compartment that corresponds to the turbocharger inlet (Figure 3).

- Extend the pole until the detent pin engages in the outer tube of the spin pole (Figure 3).

- Place the plastic tip of the spin pole against a turbocharger vane. Make sure there is no metal-to-metal contact between the turbocharger and the spin pole.

- Using the filter bag opening as a fulcrum point, apply slight downward or upward  pressure to the spin pole to begin turbocharger rotation. Inspect the turbocharger, looking for defects in accordance with current Maintenance Instructions for the Locomotive being inspected. Use a flashlight or work light to illuminate the inlet and turbocharger vane area for inspection (Figure 3).

- When turbocharger inspection has been completed, push the detent pin downward to release it from the outer tube. Push the tubes together to collapse them, and remove the pole from the Bag Filter Compartment

- Place the pole back into its normal place of storage. The rubber handle grip has a hole molded into the end to hang the pole on a peg.

- Replace the filter bags.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with all current Safety requirements.

- CAUTION:  Always make sure the plastic rotating pin contacts the turbocharger. Metal-to-metal contact could damage the turbocharger blades.

- CAUTION: Do not apply heavy pressure to spin the turbocharger. If heavy pressure is required, the turbocharger may be defective.