| TOOL AND MACHINERY GUIDE |
| --- |
| Title: Aluminum Coupler Stand | Issued By: Wulf’s Custom Welding |
|  | Prepared By: Wulf’s Custom Welding |
| Document No: 0335 |  |
| Date: September 25, 2011 | Revision: | Date Revised: |

### SUBJECT:  ALUMINUM COUPLER STAND

Capacity: The rated capacity for this fixture is 600 pounds. It may be used for either E or 
F style couplers.

FIGURE 1

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: 0335

Fixture Weight: 15 Pounds Each

Base Construction Material: 6061 Aluminum With A Delrin Wear Plate.

### DESCRIPTION:

### This stand is used to store E and F couplers in an upright position when they are removed from the draft arm.  It has no other intended uses.

INSTRUCTIONS FOR USE:

ALUMINUM COUPLER STAND:

WARNING: Ensure Blue Flag protection is applied in accordance with current operating rules before fouling any track or performing any type of repair work.

WARNING: Ensure freight car(s) is/are properly secured with hand brakes before attempting to perform remove the coupler or perform other repairs.

- Inspect the stand prior to use. The Delrin pad must be in place and tightly secured. If broken welds or other defects are found, remove the stand from service (Figure 1).

- Place the stand in an area close to the coupler to be removed. Try to position the stand so that it does not create a tripping hazard.

- Remove the coupler from the freight car. Move the coupler to the stand, placing the coupler shank in the cradle. Make sure the shank is centered in the stand before lowering it to prevent damage to the stand cradle (Figure 2).

- When repairs have been completed, pick the coupler up off the stand and place it back into the freight car.

- Place the coupler stand back into its normal place of storage.

FIGURE 2

### ERGONOMIC/SAFETY ADVANTAGES:

- Provides a secure & safe storage position, reducing tip overs.

- Easy to maneuver coupler into place.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees.

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with current Safety Rules and Regulations as required.

- WARNING: Never place any portion of your body under the coupler during handling.

- WARNING: Make sure the cradle is placed in an area that will not create a tripping hazard.

- WARNING: Keep your hands away from the coupler shank during insertion into the stand.

- CAUTION: Make sure the coupler shank is centered in the cradle before lowering to prevent cradle damage.