| TOOL AND MACHINERY GUIDE |
| --- |
| Title: Freight Car Truck Center Pin Removal Tool | Issued By: Wulf’s Custom Welding |
|  | Prepared By: Wulf’s Custom Welding |
| Document No: 0243 |  |
| Date: March 10, 2009 | Revision: | Date Revised: |

### SUBJECT: FREIGHT CAR TRUCK CENTER PIN REMOVAL TOOL

Capacity: Use to remove or install any freight car truck center pin.

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Omaha, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: 0243

Fixture Weight: 11 Pounds

Construction Material: Steel

### DESCRIPTION:

### This tool is designed to remove or install freight car truck center pins. It has no other intended uses.

INSTRUCTIONS FOR USE:

FREIGHT CAR TRUCK CENTER PIN REMOVAL TOOL:

WARNING: Ensure the freight car(s) is/are properly secured with hand brakes and/or chocks before attempting to perform any type of repairs.

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repairs.

- Inspect the fixture for defects prior to use. Make sure there are no cracks in any of the welds, and the handle is not deformed or bent. The gripping screw mechanism must be working freely.

- Turn the tool handle counter-clockwise to loosen the gripping screw so it will easily fit over the center pin (Figure 1).

- Place the tool over the center pin, and secure the pin to the tool by turning the tool handle clockwise to tighten the gripping screw. Only use hand pressure when tightening the handle (Figure 2).

- Pull the tool upward and completely remove the center pin from the bolster (Figure 2).

- Turn the tool handle counter-clockwise to loosen the gripping screw, and remove the center pin from the tool.

- Reverse the procedure to place the center pin back into the bolster.

- Remove all blue flag protection, chocks, and release the hand brake if the freight car is ready to return to service.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with current Safety Rules and Regulations as required.

- WARNING: Never use the tool for any purpose other than removing or replacing freight car center pins.

- WARNING: Keep hands and feet out from under the center pin during handling.

- CAUTION: Never apply any force other than hand pressure to tighten the gripping screw. Excessive pressure will damage the gripping screw.