| TOOL AND MACHINERY GUIDE 402-253-2772 WEBSITE: WCWRAIL.COM |
| --- |
| Title: EOTD Storage Rack Charging Bars | Prepared By: Wulf's Custom Welding |
| Document No. 0313 | Date: October 3, 2011 |

SUBJECT: EOTD Storage Rack Charging Bars

Capacity: These bars do not require a rated capacity.

| FIGURE 1 | FIGURE 2 |
| --- | --- |

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: Four Pack Bar - 0316

Six Pack Bar - 0317

Eight Pack Bar - 0318

Approximate Weight: Four Pack Bar - 26 Pounds

Six Pack Bar - 33 Pounds

Eight Pack Bar - 41 Pounds

Construction Material: Steel Schedule 80 Pipe And Fittings

### DESCRIPTION:

### This charging bar is used to provide an air supply to EOTDs for testing and battery charging. It has no other uses. It is designed to bolt on the legs of the free-standing or wall-mounted four, six and eight pack storage racks provided by Wulf's Custom Welding.

EOTD STORAGE RACK CHARGING BAR INSTALLATION INSTRUCTIONS:

- If the charging bar is ordered with the storage rack, the bar will be installed and ready to use. No installation will be necessary.

- Loosen all of the connecting bolts on the A-frame on one side of the rack. It will only be necessary to loosen one side.

- Install two of the provided square U-bolts on the front leg of the A- frame. Install the U-bolts about 1" up from the lower tube of the frame. Use the provided 1/4" backing plates, washers and nuts. Leave a gap between the A-frame and the U-bolt to allow room for installation of the charging bar mounting plate (Figure 2).

- Place the charging bar between the A-frames and slide the lower portion of the mounting plates into the gap between the A-frame and the U-bolts (Figure 2).

- Install the other set of U-bolts on the upper portion of the mounting plate (Figure 2).

- Tighten the mounting plate U-bolts and all of the fasteners on the A-frame (Figure 2).

- Remove the protective shipping cap from the rear outlet on the bar and install a compressed air source. The outlet pipe accepts 1/2" NPT fittings.

- Apply air to the bar. Remove the dust caps from all of the glad hands and open the ball valve on each valve to make sure all contaminants have been removed from the air line (Figure 4).

INSTRUCTIONS FOR USE:

WARNING: The air supply to the charging bar must not exceed ninety (90) pounds per square inch.

- Inspect the bar prior to use. All the fittings must be tight. The covers for the glad hands must be in place. Make sure the glad hand gaskets are in place and in good condition. Repair any air leaks as necessary. (Figure 1).

- Select the appropriate glad hand to use for EOTD charging. Make sure the ball valve under the glad hand is in the closed position. In the closed position, the ball valve handle is horizontal to the ground (Figure 4).

- Remove the glad hand dust cover. Open the ball valve slightly to blow contaminants out of the air line. Stand clear of the glad hand while removing contaminants (Figure 4).

- Close the ball valve completely and attach the EOTD glad hand to the charging bar glad hand (Figure 4).

| FIGURE 3 | FIGURE 4 |
| --- | --- |

- Open the ball valve, allowing air to flow into the EOTD for testing or battery charging. In the open position, the ball valve handle is vertical to the ground (Figure 4).

- When testing or charging is completed, close the glad hand ball valve by placing the handle in the horizontal position. Allow air pressure to drop off completely, then remove the EOTD glad hand from the charging bar glad hand (Figure 4).

- Place the glad hand cover back onto the glad hand to prevent contaminants or water from entering the charging bar (Figure 4).

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with Safety and General Conduct Rules as required.

- WARNING: Never apply more than ninety (90) pounds per square inch of air pressure to the charging bar. Damage could occur to the EOTD.