| TOOL AND MACHINERY GUIDE 402-253-2772 WEBSITE: WCWRAIL.COM |
| --- |
| Title: Forklift Lifting Attachment | Prepared By: Wulf's Custom Welding |
| Document No. WCW-SF - Revised | Date: November 13, 2014 |

### SUBJECT: FORKLIFT LIFTING ATTACHMENT

### Capacity: All of these fixtures are rated at a 3,000 pound working load limit.

| FIGURE 1 | FIGURE 2 |
| --- | --- |

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: 3” Tine Width – WCW-SF3

4" Tine Width - WCW-SF4

5" Tine Width - WCW-SF5

6" Tine Width - WCW-SF6

18" Extension - WCW-SF18E

Fixture Weight:  29 – 33 Pounds

Base Construction Material:  Grade 80 Lifting Components.

DESCRIPTION:

### These Lifting Attachments are equipped with a swivel lifting hook and may be used with any Forklift to lift and transport any type of materials or repair components. They are available in sizes for 3, 4, 5, and 6 inch fork tine widths. An optional 18" hook extension chain assembly is also available and may be ordered separately (Figure 2).

INSTRUCTIONS FOR USE:

FORKLIFT LIFTING ATTACHMENT:

WARNING: Ensure car(s) or locomotive(s) is/are properly secured with hand brakes  and/or chocks before attempting to perform any type of component repairs.

WARNING: Never exceed the rated lifting capacity of the attachment or the forklift.

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repair work.

- Inspect the forklift in accordance with manufacturer's recommendations and current internal inspection instructions. Remove the forklift from service if any defects are found.

- Inspect the Forklift Lifting Attachment and Swivel Hook. The tensioning knobs must be in place and moving freely. The safety chain and chain connector must be in good condition. The self-locking swivel hook must be in place and working properly (Figures 3 &5).

| FIGURE 3 | FIGURE 4 |
| --- | --- |

- Make sure the attachment width matches the forklift tine width. The attachment should grip the tine tightly after when the tensioning knobs are adjusted (Figure 3).

- Place the attachment on the forklift tine. The attachment should be placed approximately 14” away from the end of the fork tine tip to avoid fork tine bending. Attach the safety chain to any structural component of the forklift mast. Pull the attachment outward towards the end of the forklift tine to remove any chain slack (Figures 1 & 4). Do not move the attachment closer than 14” away from the end of the tine tip.

- Tighten the tensioning knobs clockwise to apply pressure to the tine. Only hand- tighten the tensioning knobs. Never use pliers or other tools to apply excessive pressure to the knobs (Figure 3).

- Open the Swivel Hook safety latch by pushing on the release button. Apply the necessary lifting device or component and close the safety latch. Make sure the safety latch release button engages the safety latch fully (Figure 1 & 5).

- Transport the material or repair component as necessary. Use caution moving components. Avoid fast starts or stops and sharp turns that could cause the load to swing (Figure 1).

- When material handling is completed, release the safety latch and remove the lifting device or component. Remove the safety chain from the mast. Loosen the tensioning knobs by turning them counter-clockwise.

- Take the attachment off the tine, and place it back into its normal place of storage.

- Remove all blue flag protection, chocks, and release the hand brake if the equipment is ready to return to service.

FIGURE 5

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees.

CAUTIONS: Noncompliance could cause damage to equipment.

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with all current Safety rules and requirements.

- WARNING: Always keep all parts of your body out from under any suspended load.

- WARNING: Always securely attach the safety chain to a structural component of the mast.

- WARNING: Always tighten the two fixture tensioning knobs before lifting.

- WARNING: Never try to make adjustments to the lifting attachment after a load has been secured.

- WARNING: Never exceed the rated load capacity of the attachment or the forklift.

- WARNING: Never start or stop quickly when the forklift is transporting a load.

- CAUTION: Never use pliers or any other tool to tighten the tensioning knobs. Using pliers could damage the tensioning knob threads.