| TOOL AND MACHINERY GUIDE |
| --- |
| Title: LONG RUNNING BOARD STORAGE RACK | Issued By: Wulf’s Custom Welding |
|  | Prepared By: Wulf’s Custom Welding |
| Document No.:0430 |  |
| Date: July 24, 2012 | Revision: | Date Revised: |

### SUBJECT:  LONG RUNNING BOARD STORAGE RACK

### Capacity: This rack has a rated capacity of 1,000 pounds.

### FIGURE 1

### TECHNICAL SPECIFICATIONS:

3Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: Long Running Board Storage Rack – 0430

Rack Weight: 350 Pounds

Base Construction Material: Steel

### DESCRIPTION:

### This rack is designed to hold long freight car repair materials including running boards. It may also be used to store hatch covers. It is not designed for storage of heavy structural steel materials.

INSTRUCTIONS FOR USE:

LONG RUNNING BOARD STORAGE RACK

WARNING: Ensure car(s) is/are properly secured with hand brakes and/or chocks before attempting to perform any freight car repairs.

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repair work.

- Inspect the rack prior to use. Remove the rack from service if any bending or broken welds are discovered.

- Using a forklift, place running boards or any other long freight car repair materials on any of the storage arms. The lower arm is designed to store wider materials (Figure 1).

- Use a forklift to remove materials from the rack for repairs as required.

### ERGONOMIC/SAFETY ADVANTAGES:

- Provides a secure method of conveniently storing long freight car repair materials such as running boards.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with Safety Rules and Regulations as required.

- WARNING: Follow all current rules and regulations regarding the operation of forklifts.

- WARNING: Keep all parts of your body away from any suspended load.

- WARNING: This rack is designed to long freight car repair materials such as running boards. It should not be used to store heavy structural steel materials.