| TOOL AND MACHINERY GUIDE |
| --- |
| Title: Side Bearing Roller Pick-Up Tool | Issued By: Wulf’s Custom Welding |
|  | Prepared By: Wulf’s Custom Welding |
| Document No.: 0263 |  |
| Date: December 29, 2009 | Revision: | Date Revised: |

### SUBJECT: SIDE BEARING ROLLER PICK-UP TOOL

Capacity: This tool is used to pick up and remove or install Side Bearing Rollers in their cages on the truck bolster. It may also be used to handle certain types of Constant Contact Side Bearing blocks.

Rated Capacity: This tool does not require a rated capacity.

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: 0263

Fixture Weight: 8 Pounds

Base Construction Material: Aluminum With Steel Grippers

### DESCRIPTION:

### This tool is used to pick up and remove or install side bearing rollers into their cages on the truck bolster. It may also be used to handle certain types of Constant Contact blocks.

INSTRUCTIONS FOR USE:

SIDE BEARING ROLLER PICK-UP TOOL:

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repair work.

WARNING: Ensure car(s) is/are properly secured with hand brakes before attempting to perform side bearing roller installation.

- Inspect the Side Bearing Roller Pick-up Tool prior to use. Make sure all the tool components are in place and working properly. The adjusting knob should turn smoothly in both directions.

- Turn the adjustment knob on the end of the tool counter-clockwise until the gripping pin is retracted far enough to pick up the bearing (Figure 2).

- Place the tool over the bearing, making sure the gripping pin is fully engaged on the bearing surface. The tool will grip equally well with the head in either the vertical or horizontal positions (Figure 1).

- Turn the adjustment knob clockwise until the gripping pin is tight against the bearing. Hand tighten the tool only. Do not use pliers or any other tool to apply additional pressure. (Figure 2).

- Place the Side Bearing Roller in the cage. Turn the adjustment knob counter-clockwise to replace the roller and allow it to drop into the cage (Figure 1).

- Use the same procedures to remove or install constant contact type side bearings.

- After repairs are completed, remove all blue flag protection, chocks, and release the hand brake if the car is ready to return to service.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees.

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with Safety Rules and Regulations as required.

- WARNING: Never place any portion of your body directly under the side bearing or contact block during handling.

- WARNING: Always handle the tool using the provided knurled surface to avoid pinch points.

- CAUTION: Never use the Side Bearing Roller tool for any purpose other than removing or installing side bearing rollers or constant contact blocks.

- CAUTION:  Only hand tighten the adjusting knob. Using pliers or other tools to apply additional pressure to the adjusting knob could severely damage the tool.