| TOOL AND MACHINERY GUIDE |
| --- |
| Title: Remote Side Bearing Gauge | Issued By: Wulf’s Custom Welding |
|  | Prepared By: Wulf’s Custom Welding |
| Document No.: 0249 |  |
| Date: December 10, 2008 | Revision: | Date Revised: |

### SUBJECT: REMOTE SIDE BEARING GAUGE

Capacity: This gauge is used to remotely measure the side bearing clearance on freight cars. It may be used from either the side or end of the car. It has no other intended uses.

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: 0249

Fixture Weight: 6 Pounds

Base Construction Material: Aluminum With Steel Gauge Fingers

### DESCRIPTION:

### This remotely operated gauge is used to measure the side bearing clearance on freight cars.

INSTRUCTIONS FOR USE:

REMOTE SIDE BEARING GAUGE USE:

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repair work.

WARNING: Ensure car(s) is/are properly secured with hand brakes before attempting to perform side bearing gauging.

- Inspect the remote bearing gauge prior to use. Make sure all the gauge components are in place and working properly. The small return spring located between the gauge fingers must be in place and applying tension.

- Turn the adjustment knob on the end of the gauge clockwise to collapse the gauge fingers to their retracted position (Figure 1).

- From either the side or end of the freight car, move the gauge into position between the truck and freight car body bolsters (Figure 2).

- Turn the gauge adjustment knob counter-clockwise until both fingers are tight against the truck and body bolster surfaces (Figure 1).

- Remove the gauge, and use a tape measure or ruler to measure the distance between the gauging fingers.

- Apply shims as necessary if the side bearing clearance measurement is not within gauge.

- Retract the gauge fingers by turning the adjustment knob clockwise and place the gauge into its proper place of storage.

- After repairs are completed, remove all blue flag protection, chocks, and release the hand brake if the car is ready to return to service.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees.

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with current Safety Rules and Regulations as required.

- CAUTION: Never use the gauge for any purpose other than measuring side bearing clearance.