| TOOL AND MACHINERY GUIDE |
| --- |
| Title: Storage Table Divider Systems | Issued By: Wulf’s Custom Welding |
|  | Prepared By: Wulf’s Custom Welding |
| Document No: MSC-021 |  |
| Date: September 3, 2011 | Revision: | Date Revised: |

### SUBJECT: STORAGE TABLE DIVIDER SYSTEMS

### Capacity: Four, six, or eight individual compartments.

| INSTALLED COMPARTMENT SYSTEM | FOUR COMPARTMENTS |
| --- | --- |

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Numbers:

Brake Shoe Table (42" X 52") Four Compartment: 0190-4

Brake Shoe Table (42" X 52") Six Compartment: 0190-6

Brake Shoe Table (42" X 52") Eight Compartment: 0190-8

Air Brake Valve Table (52" X 52") Four Compartments: 0202-4

Air Brake Valve Table (52" X 52") Six Compartments: 0202-6

Air Brake Valve Table (52" X 52") Eight Compartments: 0202-8

Fixture Weights: 63 to 128 Pounds.

Base Construction Material:  Steel dividers with Grade 5 Bolts.

### DESCRIPTION:

### These dividers are designed to compartmentalize Brake Shoe or Air Brake Valve Tables. They may be retrofitted to existing tables or ordered as an option for new tables.

### LOAD DIVIDER ASSEMBLY AND INSTALLATION INSTRUCTIONS:

- The load dividers systems come in a kit form. The kit will include all of the dividers and fasteners necessary to construct the divider system. There are four bolts, four elastic lock nuts, and eight washers required for each divider position. Complete assembly instructions will be included with every kit that is purchased.

- The flanges on the compartment dividers must face in one direction when installed. A decal is installed on the center divider that indicates what direction the divider flanges should be facing.

| SIX COMPARTMENTS | EIGHT COMPARTMENTS |
| --- | --- |

### ERGONOMIC/SAFETY ADVANTAGES:

- Ergonomically easy to retrieve parts when ready to use

- Safely stores & separates parts

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees.

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with Safety and General Conduct rules as required when assembling and installing the dividers.

- CAUTION: Make sure the dividers flanges are all turned the same direction.

- CAUTION: Make sure the elastic lock nuts are fully tightened on the bolts.