| TOOL AND MACHINERY GUIDE |
| --- |
| Title: Two-Tier Coupler Storage Rack | Issued By: Wulf's Custom Welding |
|  | Prepared By: Wulf’s Custom Welding |
| Document No: 0285 |  |
| Date: June 10, 2010 | Revision: | Date Revised: |

### SUBJECT:  TWO-TIER COUPLER STORAGE RACK

### Capacity: This rack has a rated capacity of 8,000 pounds. It will hold ten couplers.

### FIGURE 1

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: 0285

Fixture Weight: 1,050 Pounds

Base Construction Material: All steel welded construction.

### DESCRIPTION:

### This table is used to store up to ten couplers. It is designed to accept any style of E or F couplers with either standard or long shanks.

### INSTRUCTIONS FOR USE:

COUPLER STORAGE:

WARNING: Ensure car(s) are properly secured with hand brakes and/or chocks before attempting to perform coupler removal or installation.

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repair work.

- The rack consists of an upper and a lower tier. Longer shank couplers should be placed on the lower tier. Coupler guides are installed to provide an insertion reference and establish equal coupler spacing (Figure 1).

- Use a crane or forklift equipped with the proper approved coupler lifting device to move couplers into either the upper or lower tiers. Make sure you move the coupler into the rack as close as possible to a horizontal position. The coupler guides will make sure the coupler remains centered as it is pushed into the rack (Figure 2).

| FIGURE 2 | FIGURE 3 |
| --- | --- |

- Remove couplers from the rack using an approved coupler lifting fixture. Make sure the coupler is as close as possible to the horizontal position during removal.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with current Safety rules as required.

- WARNING: Keep all parts of your body out from under couplers during handling.

- CAUTION: Always try to keep the coupler as close to horizontal as possible during handling.