| TOOL AND MACHINERY GUIDE 402-253-2772 WEBSITE: WCWRAIL.COM |
| --- |
| Title: “Guru” Valve Retention Tool | Prepared By: Wulf's Custom Welding |
| Document No. 0289 | Date: November 17, 2014 |

### SUBJECT:  “GURU” VALVE RETENTION TOOL

### Capacity: This fixture does not require a rated load capacity.

| FIGURE 1 | FIGURE 2 |
| --- | --- |

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: “Guru” Valve Tool Without Protective Case - 0289

“Guru” Valve Tool Protective Case – 0289-1

“Guru” Valve Tool With Protective Case – 0289-2

Fixture Weight:  Pounds

Base Construction Material:  Steel With Plastic Warning Light.

DESCRIPTION:

### This retaining tool is used to clamp and retain the “Guru” Locomotive Water Dump Valve in the closed position while adding water to a cold locomotive cooling system, preventing the valve from inadvertently activating while water is being added.

INSTRUCTIONS FOR USE:

“GURU” VALVE RETENTION TOOL:

WARNING: Ensure locomotive(s) is/are properly secured with hand brakes and/or chocks before attempting to perform any type of component repairs.

WARNING: Ensure Blue Flag protection is set in accordance with current operating rules before fouling any track or performing any type of repair work.

- Inspect the tool before use. Make sure the adjustment knob and mechanism move freely. The red flashing LED light and lanyard should be attached and working properly (Figure 1).

- Open the jaws of the tool fully by rotating the adjustment knob counter-clockwise.

- Place the flat portion of the valve over the handle of the Guru Valve. Place the hook portion over the pipe “T” (Figure 2).

- Hand-tighten the retainer by turning the adjustment knob clockwise. Stop tightening as soon as tension is felt. Do not use pliers or any other tool to turn the adjustment knob.

- Activate the flashing red LED warning light, and attach it outside the car body using the provided magnet. Make sure the light is in a location where it will provide a visible warning that the valve is installed.

- Fill the locomotive radiator with water. Let the locomotive run long enough to allow the water temperature to rise above the point where the Guru Valve will activate (35-40 degrees).

- After the locomotive has reached a temperature to prevent valve activation, remove the Valve Retainer by turning the adjustment handle counter-clockwise. Turn off the flashing red LED warning light, and remove it from the carbody.

- Place the Retainer and light back into their normal place of storage or in the case specifically designed for the tool.

- Remove all blue flag protection, chocks, and release the hand brake if the equipment is ready to return to service.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees.

CAUTIONS: Noncompliance could cause damage to equipment.

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with all current Safety rules and requirements.

- WARNING: Use caution when working around a warm locomotive cooling system.

- CAUTION: Only hand-tighten the retainer. Never use pliers or any other tool to tighten the adjustment knob. Using pliers could damage the adjustment knob threads or the Guru Valve.