| TOOL AND MACHINERY GUIDE 402-253-2772 WEBSITE: WCWRAIL.COM |
| --- |
| Title: Freight Car Wheelset Transportation Fixture | Prepared By: Wulf's Custom Welding |
| Document No. 0149 | Date: May 28, 2010 |

### SUBJECT:

Freight Car Wheelset Transportation Fixture

Capacity: Use to transport any size freight car wheelset. The fixture has a rated 		     capacity of 4,000 pounds.

### TECHNICAL SPECIFICATIONS:

Available Through:

Wulf’s Custom Welding

19102 So. 156th Street

Springfield, NE  68059

Tel: 402-253-2772

Fax: 402-253-9092

Website: wcwrail.com

Reference Part Number: 0149

Fixture Weight: 325 Pounds

Construction Material: Steel

### DESCRIPTION:

### This fixture is designed to transport freight car wheelsets. It must not be used for any other material handling application.

INSTRUCTIONS FOR USE:

FREIGHT CAR WHEELSET TRANSPORT:

WARNING: Ensure the freight car(s) is/are properly secured with hand brakes and/or chocks before attempting to perform any type of repairs.

WARNING: Ensure Blue Flag protection is set before fouling any track or performing any type of repairs.

- This fixture may be used with any forklift having fork tine dimensions of 2” thick by 6” wide or smaller. The rated forklift capacity must be 6,000 pounds or greater.

- Inspect the fixture for defects. Make sure there are no cracks in any of the welds, and there is no bending or deformation. The mast connection safety chain must be in place and in good condition.

- Make sure all of the protective pads are in place. Any damaged or missing pad must be replaced before use to prevent wheelset or axle damage (Figure 2).  Replacement pads are available from the original equipment manufacturer.

- Attach the fixture safety chain to the mast or mast backrest assembly (Figure 2).

- Move the fixture under the wheelset and raise the mast to engage the wheelset on the fixture(Figure 1).

- Tilt the mast rearward to move the wheelset into the transport position at the rear of the fixture (Figure 1).

- Move the wheelset to the desired location. Tilt the mast forward and lower the tines. Use caution and check for personnel or obstacles when backing away from the wheelset.

- Remove all blue flag protection, chocks, and release the hand brake if the freight car is ready to return to service.

### SAFETY PRECAUTIONS:

WARNINGS: Noncompliance could cause injury to employees

CAUTIONS: Noncompliance could cause damage to equipment

NOTES: Pertinent information

- WARNING: Wear personal protective equipment in accordance with current Safety and General Conduct Rules.

- WARNING: Make sure the fixture safety chain is attached to the forklift mast or backrest before moving it under the car.

- WARNING: Make sure all personnel are clear of the wheelset and forklift during transport.

- CAUTION: Never use the fixture for any material handling purpose other than transporting freight car wheelsets.

- CAUTION: Make sure all the protective pads are in place on the handler to prevent damage to the wheelset or axle.